## Slide 1: Maker Space Session
Bluefruit Intro & Pre-Requisites

## Slide 2: Session Goals: MCU Fundamentals Install Pre-Requisites Make a blinky thing

## Slide 3: Assumptions: You have software development experience. You may not have much hardware or microcontroller experience.

## Slide 4: Maker Space Session
Fundamentals
& Intro
To Microcontrollers

## Slide 5: Introduction What is this thing?
Notes: https://www.adafruit.com/product/4333

## Slide 6: Demonstration
Notes: https://www.adafruit.com/product/4333

## Slide 7: A very full featured device. A great intro to micro controllers and programming.

## Slide 8: Key Features Blinky Lights (Neopixels) Jiggle Detection (LIS3DH) Light, Sound, Temp Sensors Beepy Thing (Speaker) Pushy Things (button, Switches) Shiny Metal (GPIO /Interface Pins)

## Slide 9: What is a Micro Controller (MCU)? A compact circuit designed for a specific single purpose, in an embedded system.

## Slide 10: Similarities to a Computer Has a CPU, Ram, and I/O* * but a lot less (Bluefruit has 2MB of Flash storage, and 32K ram- enough for a few hundred lines program. Flash can also store libraries and data structures referenced from code. )
Notes: https://www.electrokit.com/uploads/productfile/41016/adafruit-circuit-playground-express.pdf

## Slide 11: MCU vs. Computer Doesn’t run an OS Typically, only has basic interfaces (I2C, SPI, UART) Lower Power Requirements
Notes: https://www.microcontrollertips.com/microcontrollers-vs-microprocessors-whats-difference/
Protocol rundown: https://www.seeedstudio.com/blog/2019/09/25/uart-vs-i2c-vs-spi-communication-protocols-and-uses/

## Slide 12: MCU’s Commonly Used: Robotics 3d Printing, Drones, Automobiles, Cell Phones, IoT Devices
Notes: https://en.wikipedia.org/wiki/Microcontroller

## Slide 13
Notes: https://learn.adafruit.com/adafruit-circuit-playground-bluefruit/guided-tour

## Slide 14: How do you Program it? Circuit Python or Arduino/C++
Notes: https://en.wikipedia.org/wiki/CircuitPython#:~:text=CircuitPython%20is%20a%20full%20Python,selection%20of%20core%20Python%20libraries.

## Slide 15: Circuit Python: Higher Level Language (like Java or .NET) Arduino: Lower Level Language (C++)
Notes: https://en.wikipedia.org/wiki/CircuitPython#:~:text=CircuitPython%20is%20a%20full%20Python,selection%20of%20core%20Python%20libraries.

## Slide 16: Circuit Python: “Easier” to code White Space Language Arduino/C++ Lower Level, more control, Best performance, *more familiar
Notes: https://en.wikipedia.org/wiki/CircuitPython#:~:text=CircuitPython%20is%20a%20full%20Python,selection%20of%20core%20Python%20libraries.

## Slide 17: What is the Development Process?
Development
IDE/Editor
Bootloader
Program
Program
Copy file to USB
(.py)
Or “Flash” program
Via AVRDude
Notes: https://scl.utah.edu/pdf/mac_mgrs/20200219_mm/20200219_mm_hid.pdf

## Slide 18
Notes: https://learn.adafruit.com/assets/75708

## Slide 19: What about Debugging? It’s a bit more challenging on Micro Controllers w/o specialized hardware.
Serial.Print(“Here!”);
Notes: https://en.wikipedia.org/wiki/CircuitPython#:~:text=CircuitPython%20is%20a%20full%20Python,selection%20of%20core%20Python%20libraries.

## Slide 20: Circuit Python recommended Debugger (for SWD or JDAG Interface): J-Link
($20 – Non Commercial)
($400 – Commercial)
Notes: https://www.adafruit.com/product/3571?gclid=Cj0KCQiA-qGNBhD3ARIsAO_o7ynLobazrOFuuZ19zNCkEUJVh7YbmzOh0KBWZ-1dqMsDt2ntaOQijqYaAvAFEALw_wcB
(Other debuggers available for other hardware.ST Link is similar and very popular. https://www.digikey.com/en/products/detail/stmicroelectronics/STLINK-V3SET/9636028?utm_adgroup=Development%20Boards%2C%20Kits%2C%20Programmers&utm_source=google&utm_medium=cpc&utm_campaign=Shopping_Supplier_STMicroelectronics_0497_Co-op&utm_term=&utm_content=Development%20Boards%2C%20Kits%2C%20Programmers&gclid=Cj0KCQiA-qGNBhD3ARIsAO_o7ym38PhEbNY3iIcjofnmYX4hXvXQ95ajiJ_zfnhPICHstwvNeqHDIfIaAtGaEALw_wcB

## Slide 21: Circuit Python: the REPL
Notes: https://learn.adafruit.com/adafruit-circuit-playground-bluefruit/the-repl

## Slide 22: Arduino: Serial Monitor
** There is a relatively new “Arduino Extension for VS Code” Available (In Preview), allows more robust debugging of Arduino without specialized hardware.
Notes: https://marketplace.visualstudio.com/items?itemName=vsciot-vscode.vscode-arduino
https://learn.adafruit.com/adafruit-arduino-lesson-5-the-serial-monitor/the-serial-monitor

## Slide 23
Prepping BlueFruit &
Installing Mu

## Slide 24: Bluefruit Device Pre-Requisites
Install latest stable release of CircuitPython Runtime
https://circuitpython.org/board/circuitplayground_bluefruit/
Steps:
  Connect Bluefruit with a USB cable you know works with Data
  Double click middle button of Bluefruit to enter DFU mode (Device Firmware Update mode)
  Browse to the USB drive (CPLAYBTBOOT)
  Copy the .UF2 file you just downloaded to the CPLAYBTBOOT root directory (Wait for light sequence to change)
  After updating, your drive will be renamed to CIRCUITPY and you will have a few files in there (code.py, which is a "Hello World" sketch).

## Slide 25: Circuit Python Libraries (V7)
Optional- Windows Only (Driver): https://github.com/adafruit/Adafruit_Windows_Drivers/releases/tag/2.5.0.0
Download Circuit Python Libraries (v7): https://circuitpython.org/libraries
Copy over these to a folder called “lib” on your Bluefruit:
Notes: https://learn.adafruit.com/circuitpython-made-easy-on-circuit-playground-express/first-things-first

## Slide 26: Download & Install Mu
https://codewith.mu
Notes: https://learn.adafruit.com/adafruit-circuit-playground-bluefruit/the-repl

## Slide 27: Open Mu, and select “CircuitPython”

## Slide 28: Creating your first program
Save as “code.py” into root folder of CIRCUITPY USB Drive and watch the magic happen.
Notes: https://learn.adafruit.com/adafruit-circuit-playground-bluefruit/creating-and-editing-code

## Slide 29: Got it working?
Exercise 2: Modify the code to make all of the neopixels blink. Bonus points for efficient code (12 lines or less).
(Difficulty Level: Easy)
Notes: https://learn.adafruit.com/circuitpython-made-easy-on-circuit-playground-express/slide-switch
https://learn.adafruit.com/circuitpython-made-easy-on-circuit-playground-express/buttons

## Slide 30: Exercise #2
Save as “code.py” into root folder of CIRCUITPY USB Drive and watch the magic happen.
Notes: https://learn.adafruit.com/adafruit-circuit-playground-bluefruit/creating-and-editing-code

## Slide 31: Got it working?
Exercise 3: Use the switch to toggle the LED’s from blinking on and off (hint: check the status of cp.switch, which is a boolean)
(Difficulty Level: Super Easy)
Notes: https://learn.adafruit.com/circuitpython-made-easy-on-circuit-playground-express/slide-switch
https://learn.adafruit.com/circuitpython-made-easy-on-circuit-playground-express/buttons

## Slide 32: Exercise #3
Save as “code.py” into root folder of CIRCUITPY USB Drive and watch the magic happen.
Notes: https://learn.adafruit.com/adafruit-circuit-playground-bluefruit/creating-and-editing-code

## Slide 33: Got it working?
Exercise 4: Press the a button to cycle colors forward (red, yellow, green, cyan, purple, white) for all Neopixels, and the b button to cycle back to the previous set of color.
Hint: Buttons are referenced by cp.button_a and cp.button_b and have a boolean value)
Hint: Utilize an Array to define and iterate colors
Hint: Don’t forget to use REPL for helpful debugging!
(Difficulty Level: Medium)
Notes: https://learn.adafruit.com/circuitpython-made-easy-on-circuit-playground-express/slide-switch
https://learn.adafruit.com/circuitpython-made-easy-on-circuit-playground-express/buttons

## Slide 34: Exercise #4
Save as “code.py” into root folder of CIRCUITPY USB Drive and watch the magic happen.
Notes: https://learn.adafruit.com/adafruit-circuit-playground-bluefruit/creating-and-editing-code

## Slide 35: So now what?
Like the Hardware? Purchase a BlueFruit Ticket on Eventbrite (supplies limited) to buy a kit ($38). Otherwise, please return hardware to a volunteer.
Want to do more? Hang out in the Maker Space, and visit the self paced examples on the Adafruit Web Site.
https://learn.adafruit.com/adafruit-circuit-playground-bluefruit/circuitpython-neopixel
Notes: https://learn.adafruit.com/circuitpython-made-easy-on-circuit-playground-express/slide-switch
https://learn.adafruit.com/circuitpython-made-easy-on-circuit-playground-express/buttons

## Slide 36: Bluefruit Challenge
Got some spare time? Work in the Maker Space to make something awesome. Consider incorporating 3d printing and other electronics into your design.
Provide a demonstration by 1pm Friday in the Maker Space.
Awards will be given for the following (original designs only):
  Most Impressive (individual)
  Most Creative (individual)
  Most Collaborative / Best Teamwork (up to 3 people)

## Slide 37: Advanced Projects
Get a buddy and play Quick Draw- with 2 Bluefruits! https://learn.adafruit.com/circuit-playground-quick-draw/circuitpython
Pick a color with an app on your phone, and change the color of the Bluefruit (Arduino): https://learn.adafruit.com/adafruit-circuit-playground-bluefruit/ble-uart-controller
Notes: https://learn.adafruit.com/circuitpython-made-easy-on-circuit-playground-express/slide-switch
https://learn.adafruit.com/circuitpython-made-easy-on-circuit-playground-express/buttons